## Slide 1: Benefits of Recirculating Aquaculture Technology

## Slide 2: My background… (I’m an academic but…) Fingerlakes Aquaculture 1.0 million lbs per year of tilapia production located in upstate NY
Notes: Just a little about me and the farm I constructed using my and my brother’s money and a LOT of bank financing.

## Slide 3: New Species - Tilapia
360 000 tonnes (liveweight equivalent) in 2006, 1.2 kg/person
Five years ago this species was almost unknown in the US market!
Notes: US imports and consumption of tilapia is growing, some 360 000 tonnes (liveweight equivalent) were imported in 2006, which gives a per caput supply of 1.2 kg, impressive when considering that only five years ago this species was almost unknown in the market. Also in Mexico, per caput consumption of tilapia is similarly high, considering 90 000 tonnes of domestic production and a unknown quantity of imports. The Mexican market is awash with cheap and good quality tilapia from China, and local producers are suffering from this presence. On the other hand, in Europe, tilapia is still quite unknown, and total imports are stable at some 10 000 tonnes.
In the past years, China has taken over completely the US frozen tilapia fillet market. A overwhelming 85% of the US imports of this product come from China, and all the recent growth is due to exports from this country. All other supplying countries play a secondary role, with no major movements to be recorded. Maybe these countries could target the European market in future years, as the US market appears dominated by Chinese supplies. The frozen tilapia fillet from China has all the characteristics of a commodity: same size, same shape and same quality in all shipments. This characteristic makes tilapia from China the ideal product for the food service sector. The unit vale of the Chinese frozen tilapia fillets is US$ 3.00/kg, while the major competitors (Indonesia and Ecuador) are selling at US$ 5.00/kg.

## Slide 4: Why Reuse Water ?
Stricter effluent regulations
Competition for water resources
Disease and biosecurity issues
Cost effectiveness:
  optimized feeding & temperatures; stocking density
Minimize water use
  Conserve heat, reduce discharge and water source needs
Maximize bio-security
Flexibility in where farm is located (near market-Urban applications)
Notes: Tank-based production is challenged by:
  strict effluent regulations
  increased competition for water resources
    regulatory and social pressures to conserve resources
  lower farm gate prices
  disease and biosecurity issues

## Slide 5: Water Reuse Systems
Three basic types:
  serial reuse
  partial reuse
  full recirculating (0 to 15% water exchange per day)
Does not require a biofilter
Flow is reused until NH3 becomes limiting
Notes: We really focus on full-recirculating. The flow-through or serial reuse and partial reuse just exchange water (new water) to lower the contaminant loading factors. If you change more than 50% of the water per day, it is really EASY to run such a system. You’ve got to be pretty good at managing your system to do the 10 or 15% type system.

## Slide 6
Water and Land Use Issues:
Ratio of Land and Water Use for Various Systems versus
Indoor Recirculating Tilapia Production
Notes: This is a good table to give you an idea of how much more conservative a RAS is in terms of land use and water use. Note ponds (evaporation) use a lot of water.

## Slide 7
Design of a Water Recirculation System
Waste Solids Removal
Sedimentation
Swirl Separators
Screen Filters
Bead Filters
Double Drain
Aeration or
Oxygenation
Air Stone Diffuser
Packed Column
Down-flow Contactor
Low Head Oxygenator
U-tube
Fine & Dissolved
Solids Removal
Foam Fractionation
Carbon Dioxide
Removal
Air Stone Diffuser
Packed Column
Fish Culture Tank
Round, Octagonal
Rectangular or
D-ended
Biological Filtration
(Nitrification)
Fluidized Bed Filters
Mixed Bed Filters
Trickling Filters
Rotating Bio-Contactors
Disinfection
Ultraviolet Light
Ozone Contact
Notes: Basic parts to a RAS

## Slide 8
All design parameters are proportional to feeding rate
0.25 - 0.5 kg
Waste Solids
0.25 - 1.0 kg
Oxygen
0.25 - 1 kg
CO2
0.02 - 0.04 kg
NH3 & NH4
0.18 - 0.4 kg
Alkalinity
1 kg Feed
Notes: All the loading factors are proportional to the amount of fish feed being fed into the system. Hence, our first step is to calculate the feeding load for the system.

## Slide 9: Partial Reuse System - Mixed-cell Raceway
Assuming:
  Culture Density : 80 kg fish/m3
  2 tank exchanges per hour
  37 Lps from Center Drains (5 drains – 6 Lps/drain)
  147 Lps from Side Drains (5 side drains – 29 Lps/drain)
  Microscreen Filter for Solids Control (147 Lps)
35-45 kg trout/Lpm
Solids Control
Notes: To give you a sense of how much of the footprint is fish tanks and then the other stuff that makes a RAS work.

## Slide 10: Recirculating Tank System
Lab
Office
Q1
Q2
Growout 4
Growout 3
Growout 2
Growout 1
  North Carolina State Fish Barn Layout
Notes: Same idea here. A typical farm using round tanks will only use about 25% of the building footprint for the fish tanks. Mixed cell raceways instantly boost this to about 50% (or more).

## Slide 11: Design Examples – Sturgeon
MBBR
Microscreen Filter
26ft Tanks
Notes: A design that Ebeling and Timmons did recently for a client. We like this one.

## Slide 12: Design Examples – Marine Shrimp
Microbial Floc Based Systems –
Ammonia Removed by Adjusting Carbon/Nitrogen Ratio
Mixed-cell Raceways
Notes: This is a saltwater design based upon using heterotrophic bacteria to consume the ammonia being produced and providing a bacterial flock that the shrimp can graze on. Has good potential.

## Slide 13: Design Examples – Boutique Tilapia
Notes: This is a saltwater design based upon using heterotrophic bacteria to consume the ammonia being produced and providing a bacterial flock that the shrimp can graze on. Has good potential.